## Slide 1: 5 Slides About Magnetic Susceptibility
Created by Sibrina N. Collins, Lei Yang, Kari Young, Arpita Saha, Gerard Rowe, Robert Holbrook and posted on VIPEr (www.ionicviper.org) on July 18, 2014. Copyright Sibrina N. Collins, Lei Yang, Kari Young, Arpita Saha, Gerard Rowe, Robert Holbrook 2014. This work is licensed under the Creative Commons Attribution Non-commercial Share Alike License. To view a copy of this license visit http://creativecommons.org/about/license/.

## Slide 2: Learning Goals
The student will gain hands-on experience evaluating the magnetic properties of a paramagnetic metal complex
The student will be able to calculate the magnetic moment (μeff) from the magnetic susceptibility (χM) of a sample
The student will learn and understand the connection between magnetic properties, unpaired electrons, oxidation state and ligand field strength

## Slide 3: Magnetic Susceptibility Source: http://en.wikipedia.org/wiki/Magnetic_susceptibility (accessed July 17, 2014)
What is magnetic susceptibility?
According to Wikipedia:
  In electromagnetism, the magnetic susceptibility (latin: susceptibilis “receptive”) is a dimensionless proportionality constant that indicates the degree of magnetization of a material in response to an applied magnetic field.
Notes: When I want to learn about a new chemistry concept or laboratory technique, I admit I use Wikipedia as a good starting point! What is magnetic susceptibility? Why is it important? What does it really tell us? Why is it useful?

## Slide 4: What does it tell us?
Magnetic properties gives information about the number of unpaired electrons for paramagnetic metal centers
  Number of unpaired electrons
    Oxidation state of metal center
    Geometry of the metal center
    Ligand field (crystal field) strength
Notes: Why do we want to know about the magnetic properties of a metal complex? Well, knowing this information gives us information about the numbers of unpaired electrons for a paramagnetic metal center. We can then use that information to figure out the oxidation state of the metal center and geometry of the metal center. Note: Tim Hubin (University of Oklahoma) has great slides on this topic. The link to his webpage is included as a resource for this LO.

## Slide 5: What exactly is magnetism?
Any moving electrical charge with spin and orbital angular momentum generates a magnetic field in a system.
  The measurement of the magnetic response of a material to an applied magnetic field is known as susceptibility (c).
  The magnetic materials are broadly classified into two categories
    Diamagnetic (paired electrons, repelled by magnetic field)
    Paramagnetic (unpaired electrons, attracted by magnetic field)
Notes: The behavior of any magnetic material is dependent on the presence of unpaired electrons and how they interact with each other. Diamagnetism arises from the interaction of paired electrons with a magnetic field (repelled by the magnetic fields) whereas paramagnetism comes from the presence of unpaired electrons in the system (attracted by the magnetic field). The type of spin-coupling of adjacent spin pairs, further categorizes the paramagnetic materials.

## Slide 6: How can we measure the magnetic susceptibility?
Various Methods
  NMR Evans Method
  Johnson-Matthey MSB-Auto Magnetic Susceptibility Balance
  SQUID (Superconducting QUantum Interference Device)
χM = Total Molar Magnetic Susceptibility
μeff = Magnetic Moment, Bohr Magnetons (B.M.)
n = number of paramagnetic centers
Notes: The magnetic moment can’t be measured directly, but we can calculate it from the magnetic susceptibility. Various methods can be used to determine the magnetic susceptibility. Instructors: See the detailed notes on the methods in the faculty only files.)

## Slide 7: NMR Evans Method
1H NMR is a powerful tool for determination of magnetic susceptibility!
  NMR tube
    Sample solution
    Capillary with pure solvent
  NMR spectrum collected
    NMR solvent in capillary (shifted peak)
    NMR solvent in tube (reference peak)
Notes: 1H NMR is a powerful tool for determining the magnetic susceptibility of a paramagnetic compound. Developed by Evans in the late 1950s. See instructor notes (faculty only files) for more details on explaining the method to the students.

## Slide 8: SQUID Method
Superconductive quantum interference device (SQUID) is comprised of two superconductors
  separated by thin insulating layers to form two parallel Josephson junctions
  The raw data is processed to obtain molar paramagnetic susceptibility (cM).
Figure 2. SQUID Magnetometer
(Photo courtesy of Professor George Christou)
Notes: SQUID magnetometer is one of the most effective and sensitive ways of measuring magnetic properties. See instructor notes (faculty only files) for more details on explaining the method to the students.

## Slide 9: Johnson-Matthey MSB-Auto Magnetic Susceptibility Balance
A modified version of the Gouy balance
  Measuring the force change on a compact magnet upon insertion of the sample.
  Using raw data from balance, calculate mass susceptibility (cg)
  cM is then calculated from:
  cM = cg M
  (M = Molecular Weight)
Source: http://en.wikipedia.org/wiki/Gouy_balance (accessed July 17, 2004)
Notes: The MSB balance is merely a modified version of the Gouy balance. The basic idea focuses on a stationary sample and moving magnets.

## Slide 10: Calculate Magnetic Moment!
Use the calculated cM to then calculate the magnetic moment (μeff) of the sample
Compare the calculated μeff for a given metal center with the literature
  Is the result consistent with the oxidation state?
  What is the geometry of the metal center?
Notes: After calculating the molar magnetic susceptibility, you can then figure out if the result is consistent with the oxidation state and geometry of the metal center.