## Slide 1: Spectroelectrochemistry
Kyle A. Grice
Assistant Professor, Chemistry Dept.
DePaul University
hν
detector
potentiostat
detector
Notes: This presentation is meant to introduce the topic of spectroelectrochemistry to the class. Once they are familiar with the topic, they can then examine papers that involve spectroelectrochemistry and understand them in more detail. Students can also look at commercial SEC cells online or in person to obtain more information how SEC is carried out.

## Slide 2: What is Spectroelectrochemistry?
Spectroelectrochemistry (SEC) is the use of any spectroscopic method to study species that are obtained using electrochemical methods in situ.
Spectroelectrochemistry
Species that aren’t easy to isolate
Any spectroscopic method
UV-Vis
Infrared
Etc.
hν
Detector
(transmittance or absorbance)
potentiostat
Detector
(Reflectance or Fluorescence)
Notes: Spectroelectrochemistry is the study of species that are obtained in situ using electrochemistry. It is assumed that the students will have a basic understanding of electrochemistry. The spectroscopy can be many different types, but the most common are UV-Vis SEC and IR-SEC. The real power of SEC comes in observing species that are hard to synthesize and isolate, but that can be made easily in situ electrochemically. In addition, an unstable species can be made electrochemically, and then the chemical reactions of that unstable species can be observed.

## Slide 3: IR (Infrared) SEC
Two major designs:
  1) OTTLE cell – Optically transparent thin layer electrochemical cell
hν
detector
potentiostat
Working electrode is a mesh to allow IR to pass through
  2) Reflectance cell – The IR beam is reflected off of the electrode through a thin layer of solution.
hν
detector
Working
Reference
Counter
Notes: IR-SEC is a common technique that has been used extensively. Two major types of cells are used. One is an OTTLE cell, which involves performing redox chemistry at a mesh electrode then examining the species formed at the mesh. A second type involves reflecting an IR beam off of a solid metal electrode. The reflectance technique requires a well-polished electrode. The reference and counter electrodes are concentric circles, separated from the working electrode.

## Slide 4: Metal Carbonyl Chemistry
Air-stable starting material
Transient intermediates observed by IR-SEC
Species that can be isolated by chemical reduction
Various carbonyl complexes have been examined by IR-SEC
These compounds are relevant to CO2 reduction catalysis
Inorg. Chem. 2010, 49, 9283-9289 and Chem. Commun. 2012, 48, 7374-7376
Notes: An example of how IR-SEC has been used is the study of the electrochemistry of Re(bpy-R)(CO)3X-type species. These complexes are air-stable, but upon reduction result in several different species. Only the final products of the reductions can be synthesized with chemical reductants, but all of the species can be observed with IR-SEC. The carbonyls are fantastic IR reporters, so each of these species can be identified.

## Slide 5: Other Resources on SEC
Commercial Units are available
  OTTLE IR-SEC – Specac and other companies
  UV-Vis SEC – Pine and other companies
Papers with Inorganic chemistry SEC examples:
  IR-SEC: Organometallics 2014, 33, 4550-4559
  X-ray SEC: J. Phys. Chem. C 2009, 113, 308-315
  Raman SEC: Chem. Commun. 2014, 50, 5227-5229
Notes: Several resources are available to learn more about SEC. Commercial units are available. Examples include an IR-SEC from Specac and a UV-Vis SEC from Pine. A few papers are provided for students to learn more about specific types of SEC.